Mark,

Here they are, and I did (quite) a bit of testing with these.
They allow control of the individual devices In Accordance With (IAW) the Interface Standard (except in ASCII, like I said)
But taken together you can use them as a "Toolbox" to troubleshoot hardware or your own software.

1) The CmdProcessor_ASCII_2.ino has these deps:
 CmdProcessor_ASCII_InitProg_2.h
 CmdProcessor_ASCII_Shift_2.h
 CmdProcessor_ASCII_InitRegs_2.h
Save all (4) files into /Arduino/CmdProcessor_ASCII_2 and the IDE will be happy to find them for you.

2) The FB Program has almost the same name:
 FB_CmdGen_ASCII_2.bas (source)
 Load them into /FreeBasic or wherever.

3) Power up Arduino and Spectrum Analyzer, and bring up the Arduino IDE.
- The Serial Monitor will report the LO Lock States (LOCK,LOCK,LOCK, 2x)
- Shut down the Serial Monitor for now.
- Start the FB program and go through the initial setup so it can find the Metro Mini.
- When it asks for you to OPEN and then CLOSE the Serial Monitor, do it at that time.

Now continue to the FB program menu and you get choices on which devices to mess with:
"Select device from menu: "
 " 0.......For Digital Attenuator"
" 1.......For LO1"
" 2.......For LO2"
" 3.......For LO3"
" 4.......For References <60MHz Default>"
" 5.......For PLL MUX (Provision)"
" 7.......For LED's and Miscellaneous"
" 8.......To Enter a Direct Command in Hexadecimal"
" q.......To Quit"
input "Enter your choice"

4) My favorite place to start is #7 to make the LED turn on , then off. That way I know connections are okay. The idiot light test.
The CmdProcessor_ASCII_2.ino sets up the LO's for LO1=3630 LO2=3955 and LO3=270 MHz, resulting in an RF input of 10 MHz (IF1=3940MHz, IF2=315MHz and IF3=45MHz)
and that results in an RF input frequency of 10 MHz.

 But as I understand from a previous e-mail, you have 100 MHz, what to do? Easy!

5)
a) Once you get the FB program running, just set LO1=3720 MHz and LO2=3935 MHz, (LO3 will be already set at 270 MHz, and REF 1 at 60MHz will also be pre-set).
Then with 100MHz applied at the RF input, you should see a DC level of about 1.45Volts for the 45MHz Log Amp test point and a little less than that at the 315 MHz Log Amp test point.
b) Now back at the FB menu, select '0' for attenuator and enter 0dB. A DC level of 2.25 Volts for the 45MHz Log Amp test pointand 2.15 Volts for the 315 315 MHz Log Amp test point should be present.
c) Disconnect the RF input, and you will see 0.25 V on the 45 MHz log amp test point and about 0.55 volt on 315 MHz . Yup, that's great on the 45 MHz but you can see LO3 bleeding through the 315 MHz
 log amp. But we already know the fix. Just drop LO3 when reading 315 MHz.

6) Notice the choice of LO1 and LO2 frequencies.
 "Thou shalt not use a LO1 frequency that result in IF1 that is a multiple of the Phase-Frequency Detector (Fpfd)"
 So with RF=100MHz / LO1=3720 MHz we get IF1 of 3620 MHz which we then downconvert with LO2 @ 3935 MHz (and its mixer) to 315 MHz. No IF's are a multiple of 60/2=30MHz Fpfd.
 If we find ourselves in that situation, we can jump to the 100MHz ref with 100/2= 50 MHz Fpfd. If that still doesn't work, just a different Reference Divide ratio on LO1, but that will be a last resort for now.

7) What will the next versions look like? Not too many changes on the Arduino side yet, but I could do a new "FB_CmdGen_ASCII_3" that includes A2D readings through Arduino and some very basic sweeps with data recording for post-processing, similar to what we did before. Maybe some other items.

Let me know !
73!
WN2A