PROJECT 1 PUNCH LIST 10 April 2021

A	1) Compile List of Project 1 changes to incorporate on next PCB spin. / (Below is a Brief Summary, more details coming) / C115 Footprint / R200 - R201 / Filters FL300/FL302 Footprint corrections (ECS75SMF or ECS_75SMF) / T200 Footprint (modify for 90 degree rotation) / Stencil: For U203 (MAX2871) LO2, The denoting of DATA_LO2 and LOAD_LO2 are flipped: / Referring to the Schematic, at U203 / Feeding Resistor R215, change signal name From: LOAD_LO2 / To: DATA_LO2 / Feeding Resistor R214, change signal name From: DATA_LO2 / To: LOAD_LO2 / Correspondingly, At J400 Arduino Signal Header (Signal Bus) the control signals are flipped: / The signal at I/O 4 Change From: DATA_LO2 / To: LOAD_LO2 / The signal at I/O 5 Change From: LOAD_LO2 / To: DATA_LO2 / (Note: The MAX2871 chip may be erroneously labeled MAX2781X at U203 and U307) / Op Amp Scaling/Gain Offset: Not required??, just use Arduino A/D Reference Scaling??? TDB (This item is likely to be done with Arduino A/D Reference Scaling as it would be much simpler.)
A	2) Signal Analysis Spreadsheet to Shared Drive (PROJECT#1_Signal_Calculations_1.ods)
C	3) Check Digitizer Schematic
B	4) Lock Detect for Project 3 and Project 1 (This requires minor changes to both Arduino and FB Programs.)
B	5) FB and Arduino Programs for Generating Text Files from Log Amp Swept Data. / (This requires new programs, both Arduino and FB Programs, for both Project #1 and #3, depending on whether the Spectrum Analyzer or the Signal Generator is swept. These programs to be modified from existing programs)
B	6) New SPS Modules / LDO regulators to fit in existing power management footprint. Generate *.sch from current document
C	7) Order Parts for item 6 and Solder Iron
B	8) Install Puppy Linux Slacko 7.0 64-Bit in Asus Laptop.
C	9) Look into USB RF/EMI filters