PROJECT 1 PUNCH LIST 10 April 2021-Revised 28 April 2021

 1) Compile List of Project 1 changes to incorporate on next PCB spin. –--‘A’
(Below is a Brief Summary, more details coming)

a) C115 Footprint

b) R200-R201

c)Filters FL300/FL302 Footprint corrections

d)T200 Footprint (modify for 90 degree rotation)

e) Stencil: For U203 (MAX2871) LO2, The denoting of DATA_LO2 and LOAD_LO2 are flipped:
     Referring to the Schematic, at U203
        Feeding Resistor R215, change signal name From: LOAD_LO2
        To: DATA_LO2

        Feeding Resistor R214, change signal name From: DATA_LO2
        To: LOAD_LO2
Correspondingly, At J400 Arduino Signal Header (Signal Bus) the control signals are flipped:
        The signal at I/O 4 Change From: DATA_LO2
        To: LOAD_LO2
        The signal at I/O 5 Change From: LOAD_LO2
        To: DATA_LO2
 (Note: The MAX2871 chip may be erroneously labeled MAX2781X at U203 and U307)

f) Op Amp Scaling/Gain Offset: Not required??, just use Arduino A/D Reference Scaling??? TDB
   This item is likely to be done with Arduino A/D Reference Scaling. Much simpler.

2) Signal Analysis Spreadsheet to Shared Drive (PROJECT#1_Signal_Calculations_1.ods) –--‘A’

3) Check Digitizer Schematic –--‘C’

4) Lock Detect for Project 3 and Project 1 –--‘B’
  This requires minor changes to both Arduino and FB Programs.

5) FB and Arduino Programs for Generating Text Files from Log Amp Swept Data.
   (This requires new programs, both Arduino and FB Programs, for both Project #1 and #3, depending on whether the Spectrum Analyzer or the Signal Generator is swept. These programs to be modified from existing programs) –--‘B’

6) New SPS Modules/ LDO regulators to fit in existing power management footprint. Generate *.sch from current document –--‘B’

7) Order Parts for item 6 and Solder Iron –--‘C’

8) Install Puppy Linux Slacko 7.0 64-Bit in Asus Laptop. –--‘B’

9) Look into USB RF/EMI filters –--‘C’